## Slide 1: P.V.I.R Proposal Presentation
1/15/2019
Project Advisor: Lukas Graber
Stephanie Chan, stephchan40@gatech.edu
Elizabeth Fuller, efuller3@gatech.edu
Adrian Muñoz, am262601@gatech.edu
Nelson Raphael, nraphael7@gatech.edu
Lemek Robinson, lrobinson61@gatech.edu

## Slide 2: Introduction
What Is It?
Powervault Inspection Robot
Will contain a movable robot with a sensor package on arm, testing environment for expo
What is the purpose in industry?
Reduces dangers for workers and speeds up repair and maintenance of vault
Notes: Stephanie

## Slide 3: Goals
Create boards with dummy gauges that represent a powervault setup
Design remote controlled robot
Display videofeed and sensor information
Notes: Adrian

## Slide 4: Specifications
Mechanical Arm Specs
Height : Variable height from 1 - 6 feet
Degrees of Freedom : 2 degrees of rotation
Base Size : Fits in a 760mm Diameter Manhole
Sensor Package Specs
Video : Can Stream Video to GUI
Gas Sensor : Check Air Quality
IR Thermal Camera : Record Thermal Images
Microphone : Record Sounds
GUI Specs
Mobile: Usable on Mobile Platforms
Control Capabilities: Remotely Controllable Robot
Logging: Log Information
Data Streaming: Real-Time Data Streaming
Notes: Stephanie

## Slide 5: Design Approach Overview
Notes: Lemek

## Slide 6: Design Approach (GUI)
Kivy
Matlab App Builder
C#
1
Visual Graphical App Builder
2
Easy Communication to a Python System
4
Easily Exportable to IOS or Android
3
Easy Parallel Task Completion
5
Compatible with gaming controllers
Notes: Lemek

## Slide 7: Design Approach (Control System)
Perf Boards for mounting sensors
  Aren’t enough connections to need a PCB
Sensor Package protective casing
  Needs to be exposed to the air
  Needs to be water resistant
  3D printed
Speed restrictions on motors
  Restrict movement while arm is extended
  Object detection to prevent collisions
Ethernet Communication from PC to Pi
  Easiest solution for our testing environment
Notes: Elizabeth

## Slide 8: Design Approach (Mechanical Arm)
Max Extension Height
  6 ft
Degrees of Rotation
  360 degrees
Material
  Metal T-Slots
Camera Movement
  Can move up and down vertically
Lights
  Mounted to camera
Notes: Nelson

## Slide 9: Testing Procedure and Criteria
Moving robot with a controller
  Speed/direction tests
  Control/latency tests
  Xbox 360/PS3 wired controller compatibility
Mechanical Arm Mobility
  Weight distribution tests
  Total movement (up & down; rotation)
Sensors relaying data to GUI
  Accuracy tests
    Expo is an non ideal environment for practical tests
  Readability (how easy is it to interpret)
GUI
  Displays sensor data and video feed
Notes: Elizabeth

## Slide 10: Schedule
Notes: Nelson

## Slide 11: Status
GUI Design: 20% compete
Previous Robot/Sensor Package: Scrapped
Materials acquired from past project:
  Microphone w/pop filter
  2 Raspberry Pi B+
  2 Servos
  2 Motors
  Light sensor/ring light
  2 Speed controllers
  1080p WebCam
  Physical Robot
  Sensor board
Robot currently located in West’s lab
Notes: Adrian

## Slide 12: Status
Mechanical Arm CAD design: 50% complete
T-slot bars designed in Solidworks
CAD Model of Testing Environment: 95% complete
Design Schematic: 50% complete
Bill of Materials/Parts Ordering: 90% complete - On hold
Notes: Adrian